## Slide 1: CO2 laser system
M. Polyanskiy, I. Pogorelsky, M. Babzien, and V. Yakimenko
Notes: Hello world

## Slide 2: Historical perspective
Inverse
Cherenkov
accelerator
IFEL
accelerator
Thomson
X-ray source
HGHG
1995 2000 2005 2010 2015
STELLA
EUV source
PASER
30 TW
3 TW
300 GW
30 GW
3 GW
Nonlinear Thomson
scattering
Ion and
Proton
source
Thomson
X-ray imaging
LACARA
200 MeV Protons
LWFA
High gradient IFEL
20 MeV Protons
VLA
Notes: 2

## Slide 3: Ion acceleration
C. Palmer et al. Phys. Rev. Lett. 106:014801 (2011)
Ponderomotive force
drives plasma wave
Assuming l and ncr as normalization parameters, CO2 laser will produce a bubble
of 1000 times bigger volume,
at 100 times smaller plasma density,
10 times higher charge,
and better control over e-beam parameters and phasing between accelerator stages.
Laser
pulse
Electron
bunch
The ponderomotive energy of the electron in the optical field is proportional to 2.
Relativistically – strong (ao~10) 100-TW CO2 laser will be a good driver for “bubble” LWFA
Notes: 3

## Slide 4: Our priorities
1 POWER
2 RELIABILITY
{1,2} RELIABLE POWER
Notes: 4

## Slide 5: ATF’s CO2 laser
PREAMPLIFIER
REGEN
MAIN
AMPLIFIER
Pockels cell
Plasma
mirror
Kerr cell
14-ps YAG
5 ps
5 J
200 ns
20 mJ
10-ns HV
OSCILLATOR
5-ps SH-YAG
Notes: 6

## Slide 6: Increasing power: which way?
Brutal: add another amplifier section
vs.
Smart: shorten the pulse, improve energy extraction
Notes: 7

## Slide 7: First steps: isotopic active medium
Natural CO2
Isotopic CO2
Simulations
Experiment
Notes: 9

## Slide 8
Optics Express 19:7717 (2011)
Notes: 10

## Slide 9: First steps: solid-state injector
MAIN
AMPLIFIER
1-2 ps
10+ J
REGEN
400 fs
40 µJ
SOLID-STATE
INJECTOR
SIMPLICITY & RELIABILITY
SHORT PULSE
HIGH PULSE ENERGY
HIGH CONTRAST
BETTER ENERGY EXTRACTION
Notes: 12

## Slide 10: Challenge: non-linear response of IR materials
Material | n0 | n2 (10-16 cm2/W)
KCl | 1.45 | 5.7
NaCl | 1.49 | 4.4
ZnSe | 2.40 | 290
CdTe | 2.67 | -3000
Si | 3.42 | 1000
Ge | 4.00 | 2800
Kerr lensing (spatial effect)
Pulse chirping (temporal effect)
high n
low n
low n
Notes: 14

## Slide 11: Case study: n2 killing the pulse in regen
5-cm CdTe in a laser cavity
Notes: 15

## Slide 12: Regen re-configuration
YAG
R=82%
Ge, 0.5 mm
(2800×10-16 cm2/W)
IN
OUT
NaCl, 25 mm x 2
(4.4×10-16 cm2/W)
NaCl, 25 mm x 2
(4.4×10-16 cm2/W)
λ/4
IN
OUT
Polarizing splitter
ZnSe, 2 mm
(290×10-16 cm2/W)
Pockels cell
CdTe, 50 mm
(-3000×10-16 cm2/W)
BEFORE: <1 mJ
AFTER: 10 mJ
Notes: 16

## Slide 13: Next step: chirped pulse amplification
PRELIMINARY TEST
COMPRESSOR
STRETCHER
Notes: 19

## Slide 14: Saturation effects in the active medium
71 GHz
160 GHz
72 GHz
INPUT
OUTPUT
Linear regime (1.1 mJ → 1.4 J)
OUTPUT
Non-linear regime (3.2 mJ → 2.7 J)
6.2 ps
6.1 ps
2.7 ps (?)
Diffractive
grating
Pyrocamera
SPECTROMETER
Notes: 22

## Slide 15: Model simulations
88 GHz (5 ps)
170 GHz
5 ps
INPUT
OUTPUT
SPECTRUM
PULSE PROFILE
3.2 ps
(2.6 ps ?)
Notes: 23

## Slide 16: Main amplifier status
Major failure: break-down of HV fit-through between high-pressure vessel and water capacitor
Currently operating at reduced pressure and discharge voltage
Amplification loss is compensated by increasing number of passes
New mirror system featuring reliable remote control implemented
Notes: 25

## Slide 17: Long-term vision: compression to sub-ps
Laser-induced ionization shifts phase of the wave resulting in a chirp. Subsequent pulse compression results in 3~4 times pulse shortening.
Gordienko et al. Quantum Electronics, 39:663 (2009)
Spectra
Pulse profile
Notes: 27

## Slide 18: Long-term vision: optical pumping
Solid-state ErCr:YSGG (2.79 μm) laser
High pressure
No CO2 dissociation in the discharge
Direct and fast pumping of laser transition in CO2
  N2-free mixture
  Efficient energy extraction in single pass
  Eliminating self-lasing
An amplifier producing ~5 mJ output in a 3-ps pulse when pumped by a 300-mJ ErCr:YSGG laser demonstrated theoretically
Gordienko et al. Quantum Electronics, 40:1118 (2010)
Notes: 28

## Slide 19: Summary
Priority: support user’s experiments via providing reliable power
Approach to increasing power: get maximum from available amplifiers
Isotopic regen is routinely operated providing a true single pulse
New all-solid-state injector will improve system performance and reliability
Non-linear effects in optical materials becoming an issue. Regen re-configuration provided 10 mJ (2 GW) pulses before the main amplifier
Chirped-pulse amplification was a breakthrough in solid-state lasers; we expect similar impact on ultrashort-pulse gas lasers
Non-linear amplification regime in the main amplifier presumably provide pulse shortening to ~3 ps (well below resolution limit of our 20+ years old streak camera)
Main amplifier recovered from a major failure; new remotely-controlled mirror system implemented
Long-term roadmap is being considered
Notes: 30

## Slide 20: P.S.
Polyanskiy and Babzien “Ultrashort Pulses” in
“CO2 Laser - Optimization and Application”, InTech (2012)
Notes: 30