Pre-determined Confined Spaces Classifications

| Area | Hazards | Class | Certification/Permit | Testing |
| --- | --- | --- | --- | --- |
| Attics | Potential hazards are from sources not covered in Program(i.e., biohazards from rodent infestation, asbestos and fiberglass from insulation) | (Exempted from Confined Space Program) | No certification needed, but evaluation and PPE of Asbestos, Fiberglass, and biohazards required. | No atmosphere testing required |
| Crawl spaces | Potential hazards are from sources not covered in Program (i.e., biohazards from rodent infestation, asbestos and fiberglass from insulation) | (Exempted from Confined Space Program) | No certification needed, but evaluation and PPE of Asbestos, Fiberglass, and biohazards required. | No atmosphere testing required |
| Duct: Heating & Air Conditioning | By design, respirable air occupies the space under normal conditions. | Class 1 (Non-permit) | No certification needed, unless hazard is introduced, such as welding, refrigerants, coolant or cleaning solvents, or rotating blades, then certification is required. Freon, or work is going on with air handler with Freon, coolants etc. | No atmosphere testing required |
| Duct: Toxic exhaust ventilation | By design, non-respirable air occupies the space under normal conditions. | Class 2A (Non-permit) | Classification form required. | Atmosphere testing for hazards in system required |
| Air-handling fan units: HVAC or Exhaust | By design, respirable air occupies the space under normal conditions. | Class 2A (Non-permit) | If de-energized and LOTO of moving parts and stored energy: Classification form required. | No atmosphere testing required |
|  |  | Class 2C (Permit required) | If NOT de-energized or LOTO or there is a potential for occupant contact with hazardous moving parts, then permit is required. | No atmosphere testing required |
| Utility manholes containing telecommunication | Low hazard is in the space from the utility. Potential hazard arises from rusting or microbial decomposition. | Class 2A (Non-permit) | Classification form required. | Oxygen, CO and H2S testing is required to prove it is not a permitted space. |
| Utility manholes electrical | Low hazard is in the space from the utility. Potential hazard arises from rusting or microbial decomposition. Potential hazard arises from energized sources. | Class 2A (Non-permit) | If oxygen or hazardous gases reduced below hazardous levels after control measures, then certification form is required. | Oxygen, CO and H2S testing is required to prove it is not a permitted space. |
|  |  | Class 2C (Permit required) | If NOT de-energized or LOTO or there is a potential for occupant contact with hazardous moving parts, then permit is required. | Oxygen, CO and H2S testing is required to prove it is not a permitted space. |
| Utility manholes containing water | Low hazard is in the space from the utility. Potential hazard arises from rusting or microbial decomposition. | Class 2A or 2B (Non-permit) | Classification form required. | Oxygen, CO and H2S testing is required to prove it is not a permitted space. |
|  |  | Class 2C (Permit required) | If oxygen remains at hazardous levels after control measures, then permit is required. | Oxygen, CO and H2S testing is required during entry. |
| Utility manholes containing sewage | Moderate hazard is in the space from the utility posed by rusting or microbial decomposition. | Class 2A (Non-permit) | Classification form required. | Oxygen, CO and H2S testing is required to prove it is not a permitted space. If hazardous atmosphere exists, can usually be purge/vented to Class 2B. |
|  |  | Class 2C (Permit-required) | If oxygen or hazardous gases remain at hazardous levels after control measures, then permit is required. | Oxygen, CO and H2S testing is required during entry. |
| Elevator Pits | Low atmospheric hazard, respirable air occupies the space under normal conditions. High physical hazards, e.g. entrapment, contact with moving parts resulting from mechanical and electrical equipment . Verify not contiguous to source of contaminants around area such as cryogens, vehicles, or propane heaters. No oil or water in the pit. | Class 2A (Non-permit) | If de-energized and LOTO of moving parts and stored energy: Classification form required. No oil or water in the pit. | No atmosphere testing required |
|  |  | Class 2C (Permit required) | If NOT de-energized or LOTO or there is a potential for occupant contact with hazardous moving parts, then permit is required. | No atmosphere testing required |
|  | Low atmospheric hazard, respirable air occupies the space under normal conditions. High physical hazards, e.g. entrapment, contact with moving parts resulting from mechanical and electrical equipment . Contiguous to source of contaminants around area such as cryogens, vehicles, or propane heaters. Or oil or water in the pit. | Class 2C (Permit required) | If NOT de-energized or LOTO or there is a potential for occupant contact with hazardous moving parts, then permit is required, or contiguous to sources of contaminants, around areas such as cryogens, vehicle use or propane heaters; oil or water in the pit. | Oxygen, CO and H2S testing is required to prove it is not a permitted space. |