## Slide 1: GALAXIE GV-per-meter AcceLerator And X-ray-source Integrated Experiment
J. Rosenzweig
UCLA Dept. of Physics and Astronomy
BNL ATF User Meeting, April 26, 2012

## Slide 2: The GALAXIE Collaboration
UCLA Dept. of Physics and Astronomy
  Miao, Musumeci, Putterman, Regan, Rosenzweig (PI)
Stanford Linear Accelerator Center
  Tantawi
Penn State University
  Jovanovic
RadiaBeam Technologies
  Murokh, Boucher
Brookhaven National Laboratory (w/o DARPA funds)
  Pogorelsky, Yakimenko

## Slide 3: Answering the AXiS DARPA BAA
Compact, narrow-band, high flux X-ray source
  Utilize GV/m fields
  0.1% BW, set by imaging apps (e.g. phase contrast)
Efficient: Energy conversion 10-4
  Indicated in BAA
  Chooses FEL over ICS
  Sets FEL
Ultra-high brightness electron beams
  Pellegrini criterion on emittance
  Brightness for gain
Dielectric laser acceleration
Optical undulators (all optical system)
ICS illumination of “vespa” at BNL ATF
Advanced X-Ray integrated Sources (AXiS)

## Slide 4: The X-ray FEL
LCLS: First hard X-ray FEL
  Based on existing linear accelerate at SLAC
    Now working at 1.5 Å!
  Many more worldwide
  UCLA performed POP expts.
Revolutionary capabilities
  Single molecule imaging
  Coulomb explosions
  Nonlinear QED
DARPA AXIS: apply to medical imaging
  Compact and inexpensive
E=14 GeV
lr=1.5 Å
A. Murokh, et al., Phys. Rev. E 67, 066501 (2003)
courtesy G. Andonian
Saturation at VISA
~800 nm

## Slide 5
Coherence: the importance of the phase information
(a)
(b)
Amplitude of (a)
+ phases of (b)
Amplitude of (b)
+ phases of (a)

## Slide 6: UCLA core research strength: Advanced acceleration techniques
High intensity electron/laser beam excites dielectric structures or plasmas
GV/m to TV/m fields possible; scenario dependent
High energy densities: scaling of repetition rate difficult
Utilize resonant optical/IR structure acceleration
  Extend accelerator structure concept over 4 orders of magnitude in l
  Married with advanced FEL: first “5th generation” light source
  Stepping stone to higher energy applications (e.g. linear collider)
>1 TVm accelerating fields in
proposed LCLS PWFA experiment
J.B. Rosenzweig, A. Murokh, and C. Pellegrini, PRL 74, 2467 (1995)

## Slide 7: All-optical FEL
Ultra-low emittance, optically gated electron source (magnetized beam)
Low b, relativistic photonic dielectric acceletors
Optical (or THz) undulator
Long l laser source: 5 microns
Challenging integrated project
GALAXIE: Compact, High-Brightness, Monochromatic
X-rays from All-Optical, High Field Accelerators and Undulators
Traveling wave dielectric laser
accelerator
Overmoded optical undulator
Photonic defect mode
bi-harmonic structure
with 2nd order focusing
and acceleration on high
spatial harmonic
200 MV/m X-band RF gun w/flat
beam converter

## Slide 8: Long-wavelength (5 mm) laser system
Avoid aperture limitations
  Vertical emittance @ 1E-9 m level for 5 mm case (3E-11 m @0.8 mm)
  Spatial harmonic 2nd order focusing
More stable longitudinal acceleration (enlarged buckets)
  Complex dynamics from focusing spatial harmonic
Mitigate breakdown
  Small quantum energy
  Optimize at ~ps pulse length
Breakdown thresholds unknown (>GV/m?)
  Material investigations needed
Biharmonic photonic mode
dielectric structure
Longitudinal phase space (Poincare)

## Slide 9: The Accelerator Structure: Bigger Picture
Proposed silicon structure
Coupling dynamics
Monolithic plasma-etched
Si assembly

## Slide 10: 5 mm Laser Approach

## Slide 11: Mid-IR seed source setup
Palitra also at UCLA

## Slide 12: First Light at 5 mm
But we need high power for materials testing now…

## Slide 13: Optical properties, breakdown at 5 mm
Limited data exists on 5 mm light interactions
  Index, loss tangent, breakdown
  Long pulses more often studied.
    For <10 ps pulses, electrons react faster than lattice
      Avalanche ionization dominant
  Single shot vs. high rep, fluence threshold
Study critical for:
  Structure (accelerator and fabrication
  Optical components: pulse, color splitters
Candidate material crystals in hand
  CaF2,MgF2,ZnSe,Ge,Si,Al2O3
Testing ongoing at BNL ATF

## Slide 14: Diagnostic layout: Initial BNL tests
HeNe
Sample
CO2 Laser
HeNe
Det - Fast
HeNe
Det - Fast
50/50
HeNe Lens
CO2 OAP
w/ Hole
Cal.
Reference Det.
Co2 Spt.
Cal.
Cal.
CaF2
Atten.
I
t
Event
Red – He-Ne
Green – 10.2 um CO2
Purple – 5.1 um light
Doubling crystals ordered, receiv
(Altos Photonics/EKSMA)
ZGP and AgGaSe2
Joint project: UCLA, RadiaBeam, BNL

## Slide 15: IRNWA: Infrared Network Analyzer
Precision DUT measurements of 5 mm structures
New lab developed above UCLA Pegasus
Quantronix Palitra ordered, delivered, working
Upgrading current laser to 40 mJ at 800 nm; expect 0.5 mJ at 5 mm after Palitra

## Slide 16: Wakefields: 1st observation of slab structure at BNL ATF
Coherent Cerenkov radiation benchmark on mode frequencies
Deceleration/acceleration observed
Start-to-end simulations w/OOPIC
  Now extended to VORPAL 3D
Under review at PRL
Continuation of work at SLAC FACET
CCR signal and FFT
Observed (solid) and simulated
(dashed) momentum spectra
x (m)
z (m)

## Slide 17: Next step: photonic structures
Bragg, GALAXIE, woodpile structures
Both ATF and FACET planned
  Convergent with HEP program
  Advantage in fabrication at THz
Narrow, wide defects
  Optimized and Cowan-style, any axis…
Defect with optimized symmetry

## Slide 18: 1st VORPAL simulations
x
y
beam
DIMENSIONs:
Diameter of cylindrical:125 um
Beam Channel: 250um
A=350um
C=500um
a
First version: quartz tubes…
More from Gerard Andonian presentation

## Slide 19: Electromagnetic undulators
Slab and cylindrical (better for FEL) geometries
Fed by 5 mm, detuned vf structure (lu=200 mm)
  Structure construction now, beam tests at BNL ATF
  S. Tantawi reports
High effective field difficult (E and B cancel)
  also examining THz SW structure
Gap
Thickness
Width
e-
Trench

## Slide 20: Alternative: laser cut-PM undulator
3D nonlinear FEM using periodic BCs to simulate infinite array
(checked with RADIA at UCLA)
Collaboration with Arnold group (Florida)
lu: 400 µm, B0=0.34 T
Magnet width: 200 µm
Magnet gap: 200 µm
Undulator length: 2 cm
Material: laser cut NdFeB
Experiments planned at BNL
Initial testing at UCLA
Same setup as slab wakes
150 eV photon production
  F. O’Shea reports
Potential high impact on standard light sources

## Slide 21: Conclusions
GALAXIE provides new impetus to UCLA-centered collaborative work at ATF
  5 um materials testing
  Photonic/slab structure wakes
  EM undulator
  PM microundulator
Overview complemented by more detailed presentations
Materials/undulator proposal under development
  Issued after DARPA mid-year review (May 9-10)