## Slide 1: The HYSPEC Polarized Beam Spectrometer
Mark Hagen, Barry Winn, Melissa Graves-Brook
Neutron Scattering Science Division
David Anderson, Xin Tony Tong
Neutron Facilities Development Division

## Slide 2
HYSPEC People
Mark Barry Tony David
Hagen Winn Tong Anderson
Melissa
Graves-Brook
Nick
Thomas
Steve Shapiro
Igor Zaliznyak
Bill Leonhardt
At Oak Ridge Nat. Lab.
Instrument team:
Mark Hagen
Barry Winn
Melissa Graves-Brook
Lead Engineer:
David Anderson
3He Polarization:
Xin “Tony” Tong
Nick Thomas
Daniel Brown
At Brookhaven Nat. Lab.
Principal Investigators: Steve Shapiro
Igor Zaliznyak
Lead Engineer:
Bill Leonhardt

## Slide 3: Outline
What you’ve seen
What’s Hidden
What’s Coming
What’s Next

## Slide 4: Instrument Overview
Installed/Installing
In fabrication
Designed
In design
CVI
Shutter
External Building
Control Cabin
Detector Vessel & Analyzer
Sample Stage
Chopper Box B Shielding
Drum Shield
Chopper Box A
6-15m Shielding
Curved Beam Guide
15-33m Shielding
Chopper Box B
FocusingCrystals
Dance Floor

## Slide 5
What You’ve Just Seen…

## Slide 6: What’s Hidden…

## Slide 7: Choppers, Monitors, Shutters, Guides, Cables, Pipes & Socks

## Slide 8: Magnetic Guide Field in Drum Shield Exit Port
To preserve polarization of neutrons from Heusler
NdFeB magnets on the sides, steel top & bottom
Both drum shield (shown) and tertiary shutter
Inner lining: Maxus boron loaded aluminum
480 Gauss at entrance, 7 Gauss 30 cm away

## Slide 9: Cadmium Shielding inside Detector Vessel
1.5 mm thick cadmium

## Slide 10: Neutron Monitor #3
Calibrated at HFIR, so under radioactive material control
To be mounted on optical rail outside drum shield

## Slide 11: Apertures
Absorber blades: CBBC with BN paint, to be installed
Have two

## Slide 12: Flapping Ears
CBBC panels with BN paint ready to attach

## Slide 13: What’s Coming…

## Slide 14: Tanzboden
Granite tiles in US
Installers arrive next week
Air pads here, too

## Slide 15: Soeller Collimators
Both 20’ & 40’
JJ-Xray design through assembly
Dimensional Inspection Reports imminent

## Slide 16: Fine Radial Collimator
Pane angle spacing: 40’
JJ-Xray design through assembly
Dimensional Inspection Reports imminent

## Slide 17: Coarse Radial Collimator
Frame assembled by ORT-E
On-Site
Cd coated blade installation awaiting final installation

## Slide 18: Cadmium shielding at back
In addition to ½” thick CBBC panels behind tubes on 8-packs
Cadmium thickness 1.5 mm
Not shown: Cadmium sheet between 8-packs

## Slide 19: Sample rotation, tilt and translation
Huber: final design through assembly

## Slide 20: Polarized 3-He Transfer Mechanism
Basic Design: Nick Thomas
Final Design & Fabrication: Vacuum Technology International, Oak Ridge
Assembly & Testing now: Nick Thomas & Dan Brown

## Slide 21: Helmholtz-Like Coil
Technicoil: Final Design through Assembly
Currently in Fabrication

## Slide 22: Mezei Flipper
1.5 cm gap, 1 mm diameter Al wire
Fabricated parts arrive April 28

## Slide 23: Guide Field, rail mount
NdFeB magnets and steel
Parts arrive at ORNL April 28

## Slide 24: ‘L’ Shield at rolling door
Yellow Temporary Blocks currently in target building
Enables transport of largest sample environments

## Slide 25
Supermirror analyzer assembled with around 200 supermirrors
supermirror analyzer inside the magnetisation unit (500 G)
Supermirror Polarization Analyzer
Current Status:
780 out of 960 polarizers produced so far
~100 polarizers per month
200 polarizers installed in housing & tested on BOA (optics beamline at SINQ, PSI)
Anticipated completion in ~March 2011, followed by tests at SINQ
Prototype II ( 4.0 deg)
Prototype I ( 1.8 deg)

## Slide 26: Optical Rail Components
20’
40’

## Slide 27: What’s Next: Schedule
Construction complete in June 2011
Motion and Integrated testing in June 2011
IRR in Summer 2011
Neutrons in August 2011
Unpolarized commissioning through 2011
Polarized commissioning in 2012A

## Slide 28: IDT Experiments
During commissioning
  HYSPEC’s Extended Commissioning Plan (plan to demonstrate science-readiness) requires an experiment by reviewers
    Whose results may have high scientific impact
    Which exploits either the unique or the improved capabilities of HYSPEC
During operations