| Waste Description | Type of Project | Pounds Reduced, Reused, Recycled or Conserved in 2011 | Waste Type | Potential Costs for Treatment and Disposal | Cost of Recycle, Prevention | Estimated Cost Savings | Project Description Details * |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Motion sensors in Building 725 | Energy Conservation | N/A | Greenhouse Gas/Energy Conservation | N/A | $0 | $6,000 | Installation of motion-sensor lighting in hallways, restrooms, and conference rooms in Building 725. |
| LED lighting in Building 490 Conference Room | Energy Conservation | N/A | Greenhouse Gas/Energy Conservation/ Manpower | $2,940 | $4,000 | $3,710 | Forty 65-watt incandescent bulbs were replaced with LED bulbs; savings of $1,190 per year in energy costs and $2,520 per year manpower costs. |
| Sewage sludge | Publicly Owned Treatment Works (POTW) | 3,000 | Low-level Radiological Waste | $500,000 | $35,000 | $465,000 | Rad constituents were eliminated from within the Sewage Treatment Facility; the sludge is now sent to a POTW. |
| Alkaline batteries | Recycling | 174 | Industrial Waste | $10 | $0 | $10 | Two hundred pounds of alkaline batteries were collected and sent for recycling. |
| Bio-diesel tank | Alternative Fuels | 0 | Greenhouse Gas/Energy Conservation | $0 | $0 | $0 | Per DOE Order, BNL is utilizing different alternative fuels to operate maintenance vehicles. |
| Motion sensors for labs* | Energy Conservation | N/A | Greenhouse Gas/Energy Conservation | N/A | $0 | $5,817 | Installation of motion detector lighting in common areas of Buildings 490 and 463. |
| “Bio-Circle Cleaner” parts washer | Substitution | 640 | Hazardous Waste | $10,000 | $0 | $10,000 | Eliminates the need for toxic solvents, chemical storage, and disposal associated with the cleaning of vacuum parts. |
| Aerosol can disposal system | Recycling | 528 | Hazardous Waste | $42,708 | $0 | $42,708 | Empty aerosol cans are recycled as scrap, rather then sent to the Waste Management Division as hazardous waste. Eight units (F&O=5; CA=1; NSLS=1; BES =1) each handle 66 lbs of hazardous waste. |
| Electronic recycling | Electronic Recycling | 39,880 | Electronic Waste | $99,700 | $0 | $117,238 | After an extensive audit review, BNL's electronic waste (e-waste) is now collected by the Laboratory's metals recycler, which guarantees that all e-waste is recycled in the most environmentally friendly manor. |
| Electronic Reuse | Reuse | 23,287 | Electronic Waste | $58,218 | $0 | $58,218 | The Laboratory tracks electronic equipment and takes a reuse credit for transfer of equipment to another user. |
| Building demolition recycling | Recycling | 14,000,000 | Industrial Waste | $540,190 | $32,000 | $508,190 | On-site demolition products (steel and concrete) are segregated, recycled, and reused. |
| System One parts cleaner | Substitution | 1,280 | Hazardous Waste | $10,677 | $0 | $10,677 | Central Fabrications and Motor Pool each purchased a System One parts washer to re-distill dirty solvent, eliminating the need for a vendor. Removed grit and sludge are mixed with the waste oil. |
| Animal bedding conveying system | Composting | 74,000 | Low-level Radiological Waste | $780,192 | $0 | $780,192 | Animal bedding material is no longer sent to sanitary landfill; it is now conveyed to a dumpster that is emptied or composted at the stump dump. |
| Lead acid batteries | Recycled | 4,200 | Universal Waste | $29,896 | $0 | $29,896 | Avoids hazardous waste disposal costs for approximately 40 lbs. of lead per battery. |
| Short half-life waste - CA | Decay in Storage | 142 | Radioactive Waste | $48,848 | $0 | $48,848 | During 2011, 21 boxes of filters from Buildings 914 and 918 (147 ft3) were managed in accordance with BNL decay-in-storage requirements, rendering the wastes eligible for volumetric release. |
| Short half-life waste - MO | Decay in Storage | 40 | Radioactive Waste | $1,640 | $0 | $1,640 | During 2011, 5 gallons of low-level radioactive waste were managed as Regulated Medical Waste in accordance with BNL decay-in-storage requirements, rendering the wastes eligible for volumetric release. |
| Cooling Tower chemicals - MEL | Source Reduction | 4,000 | Industrial Waste | $9,000 | $0 | $9,000 | Ozone water treatment units were installed on cooling towers at the National Space Radiation Laboratory and the Relativistic Heavy Ion Collider Research Facility (1004) for biological control of cooling water. These systems eliminate the need for water treatment chemicals (typically, toxic biocides), save labor, and reduce analytical costs for monitoring cooling tower blow down. |
| Blasocut machining coolant | Recycled/ Reused | 45,280 | Industrial Waste | $110,580 | $0 | $120,180 | Central Shops Division operates a recycling system that reclaims Blasocut machining coolant and supplies it Laboratory-wide. In 2011, 5,660 gal. (45,280 lb.) of Blasocut lubricant were recycled. Recycling involves aeration, centrifuge, and filtration. This a |
| Fluorescent bulbs | Recycled | 20,220 | Universal Waste | $143,926 | $20,000 | $123,926 | Fluorescent bulbs are collected and sent to a recycling facility under the Universal Waste exemption rule. |
| Tyvek | Recycled | 92 | Industrial Waste | $4 | $0 | $11 | BNL is recycling tyvek through Garment Recovery Systems. |
| Used motor oil | Energy Recovery | 11,320 | Industrial Waste | $28,130 | $0 | $28,130 | Used motor oil from the motor pool and the on-site gas station is given to Strebel's Laundry Service to fire their boilers. In 2011, they collected 1,415 gallons of oil at no charge to BNL, which avoided the costs for disposal and 29 shipping drums ($50/drum). |
| Office paper | Recycled | 372,000 | Industrial Waste | $17,670 | $0 | $25,110 | Cost avoidance based on $95/ton for disposal as trash. |
| Cardboard | Recycled | 252,000 | Industrial Waste | $11,970 | $0 | $15,750 | Cost avoidance based on $95/ton for disposal as trash, plus $30/ton revenue. |
| Electronic Waste | Recycled | 39,800 | Industrial Waste | $1,891 | $0 | $19,393 | Cost avoidance based on $95/ton for disposal as trash, plus $200/ton revenue. |
| Metals | Recycled | 241,400 | Industrial Waste | $11,467 | $0 | $117,626 | Cost avoidance based on $95/ton for disposal as trash, plus $200/ton revenue. |
| Bottles/cans | Recycled | 45,000 | Industrial Waste | $2,138 | $0 | $2,138 | Cost avoidance based on $95/ton for disposal as trash. |
| Construction debris | Recycled | 512,000 | Industrial Waste | $14,080 | $0 | $11,520 | Cost avoidance based on $45/ton difference for disposal as trash. |
|  | TOTALS | 15,687,283 |  | $1,972,933 | $52,000 | $2,086,216 |  |
| * Cost savings of projects funded by the BNL Pollution Prevention Council will be tracked for 3 years. |