## Slide 1: Closed-loop Autonomous Research Systems ( ARES )
Kristofer Reyes

## Slide 2: Acknowledgements
Warren Powell (PI), Si Chen, Xinyu He, Yan Li, Yingfei Wang
Dr. Benji Maruyama
Dr. Michael Krein

## Slide 3: It takes an average of 20 years to go from discovery to widespread application.
After Gerbrand Ceder; Materials data from T. W. Eagar and M. King, Technology Review 98 (2), 42 (1995)
Teflon
Lithium-ion batteries
Velcro
Titanium production
Polycarbonate
Diamond-like thin films
GaAs
Amorphous soft magnets
1940
1950
1960
1970
1980
1990
2000

## Slide 4: Efforts like MGI aim to accelerate materials design and discovery through data-driven techniques
Assemble data
Generate model
Virtual screening
Identify best materials design
Test with physical experiment
Materials Genome Initiative (MGI)

## Slide 5: Data from experiments are the ultimate source of “ground truth"
Assemble data
Generate model
Virtual screening
Identify best materials design
Test with physical experiment
New materials, synthesis method, characterization
Do we have enough data?
Do we have the right data?
If we need to perform experiments, which experiments do we need to perform?
Collect the data that best helps achieve the stated design objective.
Experiments as an information collection problem:
Notes: It behooves us to accelerate the process of experimental research. Not only in terms of bandwidth and high-throughput experiments, but more along the lines of “smart experiments.”
What do I mean by smart experiments?

## Slide 6: ARES: Autonomous Research System for the study of carbon nanotube synthesis
(n,0)
(n,1)
(n,2)
SWNT
Catalyst
~1nm
Carbon nanotubes are one of the most promising & versatile nanomaterials
Broad application space: Electronic, Structural, Conductive & Sensing…
But key mechanisms during synthesis are not well understood
Notes: Unprecedented combination of mechanical, thermal and electrical properties
But carbon nanotube growth is still not sufficiently well understood
We don’t have precise control over key properties

## Slide 7: ARES autonomously executes, characterizes, analyzes and plans experiments.
P. Nikolaev, B. Maruyama, et al., npj Comp. Mat. (2016)
Kinetics
Database
Planning
Planner
Software
Laser
Raman
Vacuum
Gases In
Synthesis
ARES Controller
Characterization
Silicon Wafer

## Slide 8: Planner: Sequential Bayesian Experimental Design

## Slide 9: Planner uses Bayesian Experimental Design to select next experiments
Bayesian Experimental Design
Bayesian Optimization
Optimal Computing Budget Allocation (OCBA)
Active Learning
Optimal Learning
Prior Belief
Experiment selection
Objective function

## Slide 10: Optimal Learning guides experiments to achieve an objective
Nanotube length
Defects
Polydispersity
Objective functions
Control variables
Flow rates
Temperature
Catalyst
We need to model and learn f(x).
”Evaluating” = running experiment
Experimental results are uncertain
Ground truth can be complicated
Notes: Uncertainty in experimental results: Noise, Latent states and variables
Uncertainty in model: we don’t/can’t know everything. Complex phenomena: non-linear, non-convex, non-differentiable

## Slide 11: Optimal Learning iteratively learns the objective function through a sequence of strategically selected experiments
Decision Policy
Experiment to perform
Experiment
Experiment outcome
Bayesian update
Current Belief
Prior formation
Initial Data
Physical models
Domain expert
Temperature
Flow rates
CNT growth
Model estimates and uncertainty
Materials database

## Slide 12: Decision policies balance exploration vs. exploitation to deal with uncertainties
Knowledge Gradient
Expected Improvement
Upper Confidence Bounds
Interval Estimation
Monte Carlo Tree Search
Notes: KG = scores a potential experiment based on its power to change our estimate of the maximum objective function value.
One-step look ahead = Calculate value of experiment by enumerating potential experimental results and averaging.

## Slide 13: Estimation and uncertainties about the objective function are codified into Belief Models
Unknown quantities?
Non-parametric
Parametric models
Semi-parametric
Local parametric
Lookup table
Sampled beliefs
Linear models
Sparse additive
Belief Model =
Regression model + Uncertainty quantification

## Slide 14: Sampled belief models considers a discrete distribution on a finite sample of parameters
Assumptions
Model
Useful when using non-linear physical models
Simple calculations
Need to hill-climb (resample)
Susceptible to model misspecification
Notes: “Candidate models”

## Slide 15: As more data is collected, the distribution on parameters becomes more refined
S. Chen, K. Reyes, et al. SIAM J. Uncertainty Quantification (2015).
Prior belief
1 experiment
2 experiments
3 experiments
Maximize stability of an emulsion
Reaction-diffusion model of emulsion stability.
Three kinetic parameters
KG policy to select experiments

## Slide 16: Local parametric models avoid model misspecification
Local parametric models
Global models
“Stitch local models together”
Pressure
Temperature
Non-adaptive
Hard to get right
Notes: Misspecification risk high when dealing with complex systems:
(ARES + CNT): Phase change phenomena, catalyst np activity, gas and surface reactions.
Idea with local models: Model dominant processes in a local region, assumption that local models are simpler than global.
Several local models l(x, theta), assigned to local regions in experiment space, and stitched together with Gaussian radial basis functions

## Slide 17: Belief models and policies are evaluated using Optimal Learning simulations
Decision Policy
Experiment to perform
Noisy measurement from truth
Experiment outcome
Bayesian update
Current Belief
Generate ground truth
Model / policy performance

## Slide 18: Average opportunity cost measures how far from optimal a policy achieves after a fixed number of steps.
True best experiment
Estimated best experiment
Opportunity cost
Truth
Estimate
Objective function
Experiment space
Number of experiments
How far from optimal?
Optimal Learning with Local Nonlinear Parametric Belief Models over Continuous Designs, X. He, K.Reyes, W.B. Powell

## Slide 19: In addition to ARES, we’ve applied Optimal Learning to a diverse set of problems
Wang, K. Reyes, K. A. Brown, C. A. Mirkin, W. B. Powell, SIAM J. Scientific Computing, Vol. 37, 2015.
Optimizing optoelectronics
J. Vazquez-Anderson, M. K. Mihailovic, K. C. Baldridge, K. Reyes, K. Haning, S. H. Cho., P. Amador, W. B. Powell and L. M. Contreras. Nucleic Acids Research, 2017.
Identifying information-rich regions in large RNA molecules
K. Reyes, S. Chen, Y. Li, W. B. Powell, Proc. of the TMS Annual Meeting, 2015
Increasing measurement noise
Probability of Success
Measurement noise (%)
Measurements
Analyzing risk in Optimal Learning campaigns
Better performance

## Slide 20: Key take-aways
ARES autonomously executes, characterizes, analyzes and plans experiments.
Planning is done by sequential Bayesian experimental design
Optimal Learning with the KG policy uses a one-step look-ahead to pick the experiment with highest marginal value of information.
Proper prior formation and uncertainty quantification is important for good decision making.

## Slide 22
KG

## Slide 23: The Knowledge Gradient policy scores potential experiments on their power to change the estimation of the maximum objective function value
Maximum value based on current belief
The experimental outcome if we choose “x” as the next experiment
The posterior estimate given experimental outcome
Maximum value based on posterior belief
Weighted average over potential outcomes
: “future”
: posterior estimate of
: “now”
: prior estimate of
Notes: Useful pneumonic: KG = estimated posterior max minus the prior max.
One-step look-ahead policy: Approximate the value of a potential experiment by enumerating all possible outcomes and averaging.
Deceptively simple.

## Slide 24
INSIGHTS

## Slide 25: Insights for autonomous experimental design and optimization

## Slide 26: Uncertainty quantification is important
Uncertainty in experimental results
  Noise
  Latent states and variables
  Experimental reproducibility
Uncertainty in belief models
  Unknown parameters
  Model specification
Notes:   Uncertainty in regression function: we don’t/can’t know everything

## Slide 27: Many Optimal Learning calculations are embarrassingly parallelizable
Examples:
  KG values – Monte Carlo estimations
  Monte Carlo Tree Search policies
  Sampled belief model
Computational resources not onboard ARES
  Web-based API to compute servers
  https://hds.princeton.edu/demos

## Slide 28: Scientific data comes equipped with useful prior knowledge
How do we incorporate physics knowledge as prior information?
Currently: Physical model with unknown parameters
  Model misspecification
  Research itself, not autonomous
Can we learn the model as we go?

## Slide 29
AUTOMATED MODELS

## Slide 30: Can we learn the model itself?
Semi-automated learning of chemical reaction networks
Notes: Use models with variable but parametrical structure, and learn the structure.

## Slide 31: Use chemical reaction networks instead of general machine-learning techniques.
Neural Network
Parameters = network weights
Network structure is layered
Chemical Reaction Network
Parameters = reaction rates
Network structure determined by reaction stoichiometry equations

## Slide 32: Chemical Reaction Networks
A CRN dictating the reaction rates between S species and R reactions is determined by:

## Slide 33: Kinetic equations
Mass-action kinetics
For each species, we let xs(t ) represent the concentration of species s at time t.

## Slide 34: Relevant species for the CNT problem
Precursor gases
C2H4
CO2
H2
H2O
Phase species
CNT: “Carbon adsorbed onto CNT”
Cat: ”Catalyst NP Lattice sites”
Other species?
Junk Carbon/Platelet that decrease Cat sites?
Gas phase products of pyrolysis?
Something else?
Problem: Can we learn the existence of other species and reactions to explain observations?

## Slide 35: What is correct structure/parameters for CNT kinetics?
We attempt to fit structure/parameters to growth curves obtained experimentally.
Nested optimization problem:
Structural parameter
Continuous parameter
Experimentally observed growth curves

## Slide 36: Outer optimization over CRN structure
We optimize using simulated annealing (SA).
Possible “mutations” to an existing structure:
  Add a reaction
  Remove a reaction
  Add a species
  Remove a species
  Change the stoichiometry of an existing reaction
SA algorithm
  : start with 6 species (precursors + CNT + Cat) and no reactions.
  Until convergence:
    Mutate current structure:
    If ) < )
      Accept mutation
    Otherwise, accept mutation with some probability.

## Slide 37: Inner optimization is classical constrained optimization
fmincon in MATLAB.
Box constraints on prefactors and energy barriers
  (s-1)
  (eV)

## Slide 38: We can fit individual curves for various observed growth modes.
C2H4
H2
CO2
H2O
Cat
CNT
X1
R1
R2
Time (s)
CNT Growth

## Slide 39
C2H4
H2
CO2
H2O
Cat
CNT
X1
X2
R1
R2
R3(a,b)
Time (s)
CNT Growth

## Slide 40
C2H4
H2
CO2
H2O
Cat
CNT
X1
X2
R1
R2
R3(a,b)
Time (s)
CNT Growth

## Slide 41
C2H4
H2
CO2
H2O
Cat
CNT
X1
X2
F2
R5
R1
R3
R4
Time (s)
CNT Growth

## Slide 42: Searching over graph structures is hard
Optimization inner-loop requires integrating stiff dynamics.
  Current work: Can we optimize physical parameters during integration?
Simulated annealing outer-loop doesn’t explore graph structures effectively.
  Current work: Develop more continuous mutations (e.g. identifying and simplifying multistep reactions into several elementary ones).
  Current work: Need good “initial guess” – must come from this community.
Mass-action kinetics may be too simplistic.
  Future work: Instead of graph of species/reactions, consider a graph of potentially relevant physical mechanisms (nucleation, ripening, adsorption, etc.)
Notes: Take advantage of problem-specific structure