## Slide 1
NYSDS2018
Guangwei Che
Scientific Data and Computing Center
Brookhaven National Lab
Performance Evaluation for Tape Storage Data Recall with T10KD Drive

## Slide 2: Agenda (1)
Purpose of the Performance Evaluation
SDCC Tape Storage Overview
HPSS Community Data Size Ranking
What is RAO and TOR
Test Environment and Setup
Test Cases and Configuration
Test Results and Analysis
Summary and Conclusion
Q & A

## Slide 3: Purpose of the Evaluation (2)
Tape storage is the best solution for archiving big data due to high capacity, low cost and long retention.
As the nature of sequential media, the main drawback versus disk storage is the slow performance for data recall in random access order
With emerging of the modern technology, new solutions from both hardware and software are developed to improve the data recall performance.
Finding the best solution for SDCC mass storage becomes more challenging and imperative

## Slide 4: SDCC Tape Storage Overview (3)
Serves a worldwide scientific community since 1998
Facilitate and store more than 100 (142) PBs data for RHIC and LHC and many other scientific org.
Managed by High Performance Storage System (HPSS), a software which is developed in 1990s by IBM in collaboration with various DOE National Labs
Ranked 2nd largest HPSS site in the US, 4th in the world

## Slide 5: HPSS Community Data Size Ranking (4)
Sites | Data PBs | Last update date | HPSS in prod. since
ECMWF (European Centre for Medium-Range Weather Forecasts) | 363.25 | 7/17/2018 | Nov 2002
UKMO (United Kingdom Met Office) | 253.06 | 7/10/2018 | Jun 2009
NOAA-RD (National Oceanic and Atmospheric Administration Research & Development) | 144.09 | 7/11/2018 | Nov 2002
BNL (Brookhaven National Laboratory) | 142.39 | 7/03/2018 | Sep 1998
LBNL-User (Lawrence Berkeley National Laboratory – User) | 136.54 | 7/05/2018 | Mar 1998

## Slide 6: What is RAO and TOR (5)
Tape recall: restore data from Tape to disk buffer for user’s access
Linear Tape Open (LTO) tape drives support file offset ordered recalls. However, sequential media nature result in long seek times between file reads.
The example below illustrates a 316 seconds of file seeking time:

## Slide 7: What is RAO and TOR (6)
Enterprise tape drives now support Recommended Access Ordering (RAO).
Multiple tape recalls are properly ordered by the tape drive to reduce recall time.
This same example illustrates now only 126 seconds file seeking time in RAO drives, overall file access performance increased by 151%

## Slide 8: What is RAO and TOR (7)
A new feature named Tape Ordered Recall (TOR) introduced in HPSS7.5.1 release.
It supports both RAO and non-RAO drives
TOR will use RAO feature if available. Otherwise, it makes a linear offset ordering to recall the data.

## Slide 9: Test Environment and Setup (8)
HPSS core and gateway server: RHEL6.9, HPSS7.5.1p2u1, DB2v10.5p8
HPSS mover and pftp client server: RHEL6.9, HPSS7.5.1p2u1
Tape Library: Oracle StorageTek SL8500 Modular Library System
Oracle Automated Cartridge System Library Software (ACSLS): 8.4.0
Tapes and drives: Oracle T10KD, firmware: 4.13
All tests performed as stage only, no network data transfer was involved

## Slide 10: Test Cases and Configuration (9)
Big file test
800 big files of 10 GB, total 7.81 TB data migrated to a T10KD tape
Small file test
4000 small file of 1 GB, total 3.91 TB data migrated to a T10KD tape
Aggregated small file test
2000 small file of 1 GB, total 1.96 TB data migrated to a T10KD tape

## Slide 11: Test Cases and Configuration (10)
HPSS setting
TOR: by default TOR is enabled
Noschedule: TOR is disabled
Nodrive: RAO is disabled
Recall coverage
The percentage data recalled out of the whole tape: 10%, 50% and 100%
Recall tools and settings
HPSS scrub (stagebatch), HPSS quaid, ERADAT (= Efficient Retrieval and Access to Data Archived on Tape)

## Slide 12: Test Results and Analysis (11)
Big file staging test result
Chart: Fig. 3: 10GB Big File non-aggr Test
| Staging rate MB/s.drv Noschedule | Staging rate MB/s.drv Nodrive | Staging rate MB/s.drv RAO | Staging rate MB/s.drv Quaid | Staging rate MB/s.drv ERADAT - Nosched | Staging rate MB/s.drv ERADAT - TOR
10% 80 files | 136.74 | 133.22 | 208.87 | 0 | 123.96 | 208
50% 400 files | 136.31 | 133.47 | 227.64 | 0 | 180.17 | 228.39
100% 800 files | 133.94 | 133.84 | 224.46 | 247.53 | 253.18 | 253.95

## Slide 13: Test Results and Analysis (12)
Big file (10GB) non-aggregated recall
ERADAT has the best performance. In 100% recall, ERADAT performs the best: 253 - 254 MB/s.drv
Quaid ranks second: 247.53 MB/s.drv,
RAO ranks third: 224.46 MB/s.drv
Noschedule and nodrive rank last: 133.94 MB/s.drv and 133.84 MB/s.drv respectively.
ERADAT TOR mode for partial recall performs better than nonTOR mode. For 10% and 50% staging test, TOR mode performs 68% and 27% better than nonTOR mode.

## Slide 14: Test Results and Analysis (13)
Small file non-aggregated staging test result
Chart: Fig. 4: 1GB Small File non-aggr Test
| Staging rate MB/s.drv Noschedule | Staging rate MB/s.drv Nodrive | Staging rate MB/s.drv RAO | Staging rate MB/s.drv Quaid | Staging rate MB/s.drv ERADAT - Nosched | Staging rate MB/s.drv ERADAT - TOR
100% 4000 files (nosched: 2000) | 27.21 | 32.48 | 105.67 | 184.97 | 252.14 | 249.01

## Slide 15: Test Results and Analysis (14)
Small file (1GB) non-aggregated recall
ERADAT has the best performance: 249 – 252 MB/s.drv
Quaid is the second: 184.97 MB/s.drv
RAO is the third: 105.67 MB/s.drv
Nodrive is the fourth: 32.48 MB/s.drv
Noschedule is the last: 27.21MB/s.drv
Nodrive performs 19% higher than noschedule mode.

## Slide 16: Test Results and Analysis (15)
Small file aggregated staging test result
Chart: Fig. 5: 1GB Small File aggr Test
| Staging rate MB/s.drv Noschedule | Staging rate MB/s.drv Nodrive | Staging rate MB/s.drv RAO | Staging rate MB/s.drv Quaid | Staging rate MB/s.drv ERADAT - Nosched | Staging rate MB/s.drv ERADAT - TOR
100% 2000 files | 20.35 | 68.61 | 20.45 | 74.86 | 253.75 | 224.49

## Slide 17: Test Results and Analysis (16)
Small file (1GB) aggregated recall
ERADAT still has the best performance: 224.49 – 253.75 MB/s.drv
Quaid ranks second: 74.86 MB/s.drv,
However, nodrive ranks third now instead of RAO: 68.61 MB/s.drv
RAO has the same performance as noschedule mode and ranks the last: 20.45 MB/s.drv and 20.35MB/s.drv respectively. As RAO is unable to recognize the file offset, not working anymore.
ERADAT nonTOR mode performs also better than TOR mode.

## Slide 18: Summary and Conclusion (17)
100% recall performance ranking
Chart: Fig. 6: 100% Recall Performance Ranking
| Big file (10GB) stagingTest | Small file (1GB) stagingTest | Aggregated Small file (1GB) stagingTest
Staging rate MB/s.drv Noschedule | 133.94 | 27.21 | 20.35
Staging rate MB/s.drv Nodrive | 133.84 | 32.48 | 68.61
Staging rate MB/s.drv RAO | 224.46 | 105.67 | 20.45
Staging rate MB/s.drv Quaid | 247.53 | 184.97 | 74.86
Staging rate MB/s.drv ERADAT - Nosched | 253.18 | 252.14 | 253.75
Staging rate MB/s.drv ERADAT - TOR | 253.95 | 249.01 | 224.49

## Slide 19: Summary and Conclusion (18)
In summary
Tape Ordered Recall (TOR) is a great feature to enhance the random access recall’s performance. It works effectively for both enterprise drives with RAO support and non-enterprise (LTO) drives.
RAO will not work with aggregated tape recall. As it can not recognize the file offset within the aggregate.
Quaid has even better performance than TOR in all cases tested. However, as it is a command line tool, customization script is needed for advanced usage and implementation.
ERADAT is proven to be the best performer among all recall tools tested, especially for aggregated small file recall.
Given SDCC’s data characteristics, ERADAT definitely is the best solution to handle both large amount of aggregated and non-aggregated data.

## Slide 20: SDCC Tape Library Pictures (19-1)

## Slide 21: SDCC Tape Library Pictures (19-2)

## Slide 22: SDCC Tape Library Pictures (19-3a)

## Slide 23: SDCC Tape Library Pictures (19-3b)

## Slide 24: SDCC Tape Library Pictures (19-4)

## Slide 25: SDCC Tape Library Pictures (19-5)

## Slide 26: Q & A (20)
Questions ????