M. Friedl, H. Pernegger

Phobos Spectrometer 
Module Tests

Phobos Collaboration Meeting

BNL, Apr 16–18, 1999

Contents

Introduction

Calibration and Source Test

Calibration Details

Module Studies

Signal

Noise

Signal-to-Noise

Summary

Introduction

Terminology:

1 or 2 hybrid(s) + 2 to 4 sensors = 1 module

Status:

Assembly of Phobos Spectrometer finished

(42 installed modules)

Calibration and Source Test

2 module tests:

Calibration (performed on all hybrids and on all modules)

Source Test (performed on final modules)

Why calibration?

Testing, immediately repairing bad bond wires etc. before any further assembly step

Obtaining gain (calibration) of every single channel (spectrometer including spares: 68k)

Find defect and noisy channels

Why source test?

Final module test, similar to beam operation

Study module properties

Determine signal and signal-to-noise

Measured data is filled into the Assembly Database (accessible via Phobos Web pages)

Calibration Details

Step pulse over capacitor

(Q = C (V

Ex.: 1 mV on 2 pF gives 12500 e-

Design considerations to minimize noise

Output parameter: Channel gain [mV/fC]

Calibration test setup

Hybrid/Module

Adapter board with step DAC and pulse generator board (E. Griesmayer, H. Frais-Kölbl), range 0..350 fC, diff. lin. better than 1%

CERN Repeater cards (A. Rudge)

NIM sequencer logic

National Instruments ADC board

PC running LabView

Calibration components

1 capacitor is located close to each VA chip on the hybrids

Switching logic is integrated in the VA chips

Gain Uniformity

Within 1 chip: <3% pp

Chip-to-chip: <15% pp

Calibration allows to indentify

good channels

pinholes

channel shorts

Calibration modes

“Standard”: done on every hybrid and module, running for about 6 months

“Precision”: done on selected modules, special effort on stability and parameter settings, done for module properties measurements (running for a few days)

Calibration repeatability

Standard: <3% (no effort to maintain voltages like FEC)

Precision: <1% (as expected with FEC)

No charge loss due to detector capacitance

Could be calculated from calibrations of hybrid (w/o sensor) and module (w/ sensor) to see large effects >10%

Detector capacitance: 25 pF (typ.)

VA input capacitance: not measured

Charge loss below standard mode error 
( VA input C >> detector C

Sample gain map for MOD20001

Comparison of average chip signals without and with channel calibration

Module Studies

Levels of study

Single sensor level

Single module level

Module/sensor comparison level

Typical example: MOD20001

4 sensors (thicknesses 308..310 m)

5 rows, 400 columns

Sensor level

Sensor signal distribution (norm. to 300m)

Fit function: Landau convoluted with Gaussian

Gaussian sigma represents electronic noise and intrinsic detector fluctuations, typically about 2x electronic noise

Peak of convolute is slightly shifted from pure Landau peak (MP)

Sensor RMS noise map

Sensor MP signal vs. row

Module level

Signal and SNR distributions (norm. to 300m)

MP = 21523 e- = 77.9 keV

SNR = 16.4

Relative MP signal vs. row

Uniformity better than 1% pp !!!

Signal

Absolute MP signal vs. sensor type (normalized to 300 m thickness)

Acquired with 90Sr  source

Average source signal: 21081 e-

Signal range: 20119..21552 e-

Signal MP agrees with capacitive loss calculation (charge sharing between detector and VA input capacities)

Relative MP signal vs. row

Uniformity: <1%

Very uniform even though readout lines vary in length (3..65 mm)

Mystery

3% (1% at testbeam) difference between front and back half of hybrids

Intrinsic module property, reason: ?

We can exclude external effects because:

Calibration and source tests are done with the same set of repeater boards

Switching the ADC channels does not change anything

Same (though smaller) effect in testbeam with totally different DAQ hard- and software

Noise

Single channel physical connections

Single channel preamp noise model

| symbol | represents | typ. value |
| --- | --- | --- |
| ILeak | Fraction of sensor leakage current | 5 nA |
| RP | Parallel resistance (polysilicon) | 2 M |
| C | Capacitance of pad against backplane, between pads and between metal 1 and metal 2 layers | 25 pF |
| RS | Effective serial trace resistance | 40  |
| TP | Shaper peaking time | 1.2 s |
| ENCC | Preamp noise (k + C · d) | 950+5/pF e- |

Total preamp equivalent noise charge

Contributions

with ENC [e-], k [e-], d [e-/pF], 
ILeak [nA], TP [s], RP [M], RS []

Preamp noise with typical values (as stated above)

| ENCC = | 1078 | e- |
| --- | --- | --- |
| ENCILeak = | 249 | e- |
| ENCRP = | 562 | e- |
| ENCRS = | 60 | e- |
| ENC = | 1243 | e- |

Shaper/Buffer and readout noise adds to preamp noise

Estimated shaper/buffer noise: 100 e-

Measured test setup readout noise: 450 e-

Calculated and measured noise vs. sensor type

Calculation and measurement agree very well

Measured RMS noise:

Average noise: 1383 e-

Noise range: 1230..1517 e-

Signal-to-Noise

SNR vs. Sensor Type (normalized to 300 m)

Measured SNR:

Average SNR: 15.2

SNR range: 14.4..16.9

Summary

Stable calibration and source test setups

Gain of every single channel written into assembly database

Gain uniformity: 
<3% pp within chip, <15% pp chip-to-chip

Calibration repeatability during tests
<1% precision

Gain before and after sensor mounting is the same within error bars

No significant charge loss by detector capacitance

Due to large VA input capacitance

Mystery

3% signal difference between hybrid halves

“The general picture”

Landau-Gaussian convolute fit function

Typ. values (MOD20001):

MP signal (90Sr source) = 21500 e-

RMS noise = 1347 e-

SNR = 16.0

The sensor properties:

Signal (normalized to 300 m thickness)

Average MP signal: 21081 e-

Signal range: 20119..21552 e-
(depending on sensor type)

Uniformity: Signal vs. row <1% on all sensor types ( very uniform!!!

Noise

Primarily depends on detector capacitance

Average RMS noise: 1383 e-

Noise range: 1230..1517 e-
(depending on sensor type)

Agrees very well with model

Signal-to-noise (normalized to 300 m thickness)

Average SNR: 15.2

SNR range: 14.4..16.9
(depending on sensor type)

# Footnotes

P. Shulek et al., Sov. J. Nucl. Phys. 4, 400 (1967)

# Text boxes

“Left”
Hybrid

“Right”
Hybrid

Silicon Sensors

Source particle

VA-HDR1

DAQ

90Sr source

Si
Sensor

Trigger
Scintillator

Voltage

Step

Generator

## Calibration
Capacitor

Columns

Origin

Corner

DAQ

VA-HDR1

Rows

3 parameters:

## Width, MP, Area

1 parameter:

Sigma

RP

+HV

RS

RP

Sensor

ILeak

C

TP

ENCC

## Detector
Capacitance