Installation of Octagon Detector

I)	Setup

No jewelry, watches, or loose sleeves.

Long hair tied, shoe laces tied.

Shirts tucked in properly, nothing loose in shirt pockets.

Floor cleared ( from Chemistry building to the car and in tunnel)

All other people should be clear from the area

No passage of anyone through the area during operation or crossing area to transportation.

Only 1 person will speak at a time, usually the persons leading the action or the person who is performing a certain action ( releasing handles, pin in place, etc)

Whenever someone sees a problem, then this person SHOULD SAY STOP. The response of the other people will be that they freeze.  Action will only proceed after the person who issued the STOP has explained and the problem is resolved.

Police escort ready in parking lot

- Arrangements have been made with Connie that no deliveries are made in parking lot.

Hallways in 1010 clear.

II)	Transport from Chemistry Building to the tunnel

Personnel: Alan, Birger, Mike, Rachid, George, Bolek, Nigel

Start position in Chemistry building

Assembled Octagon sitting on the table in middle of Chemistry Si-Lab

Bolek in the hallway

Door to lab completely open and secured

Door to parking lot open and secured by George

MIT van backed up in parking lot - bubblewrap installed in center of van, rear gate open

Birger and Rachid holds front handles, Alan rear handles

Nigil walks in front, Mike in back

Bolek gives 'all clear' instruction

Carriers walk through door to hallway, through hallway to parking lot and wait behind van.

George and Nigel enter van to receive octagon

Birger & Rachid hands over front end to George and Nigel

Birger and Rachid reaches under box for support

Octagon is placed in cushioning material in van

George and Nigel exits rear of van.

Rachid enters van from rear, Birger through right side.

Alan closes rear door from outside.

George drives van - Alan is passenger.

Bolek, Mike, and Nigel drives to 1010 area to prepare

Drive 5 mi/hour the following route: Chemistry rear lot; Cornell Avenue east; drive toward 1010 area via Brahms (counter clockwise).

Van parked with rear facing east door of 1010A.

Rachid and Birger stays in van.

III)	Preparations in 1010 Area

Personnel: Bolek, Mike, and Nigel

take the fence down.

open left side of door in maze in hallway

inspects passageway to tunnel

install plastic mesh barrier in 9 o'clock end of tunnel

IV)	Moving into tunnel

D - Start position: Bolek controls area inside 1010A.  Everybody else near van

Bolek gives all clear signal

Alan open rear gate of van

Rachid and Birger exits van

Alan enter van through side door

Nigel and George behind van, and Alan start lifting out

Nigel and George pass to Birger and Rachid, reach in and lift under rear of box, move away from van

Alan exits van and takes over rear handles

George tends entrance door to 1010A

Carriers walk through parking lot, 1010A building up to gate with Nigel in front

Mike opens and tends gate

Bolek holds maze door

Carriers proceed through tunnel with Nigel in front

Carriers place octagon on table A (see definition below)

- George and Mike put up plastic mesh barrier to Phobos IR at 11 o'clock side

- Rachid and Birger installs cover w. open end for cables

George supervises re-installation of fence

Rachid guards octagon during re-installation of fence

V)	Testing of octagon in tunnel

Personnel: Pradeep, Rachid, Alan, Heinz- only basic functions are tested ( pedestal, noise )

VI)	Installation of octagon on beampipe- Preparation

Personnel: Alan, Birger, Rachid, Mike, Russell, Bolek, George

Table A: Just inside fence with octagon on top

Table B; Next to beamline with octagon support on top

Table C: Next to cooling system on opposite side of beamline

On table A: Place transport box with octagon detector on inner half of table

Place spare transport plate on outer half of table; same orientation

Whole fence removed on 9 o'clock side

VII)	Separation of top and bottom halves

Personnel: Alan, Birger, Rachid, Mike, Bolek, George

Bolek reads off checklist

Russell observes and guards hallway

Initial: Octagon in test box on table A on inner half

Spare transport bottom along side octagon on outer half, same orientation

George supervises removal of fence while Rachid guards octagon

Rachid, Alan remove plexiglas box, while Birger secures bottom plate

Store cover under table A

Rachid and Alan support upper half from both ends

Birger remove screws holding top and bottom together

Rachid and Alan separate upper and lower half (Birger and Russell hold down board) - move to outer side

Place mylar on top for protection

Birger installs handles while Rachid and Alan hold top half

Rachid and Alan place top halves onto spare bottom plate.

- Birger secures handles on transport plate -	installs cover

George makes sure passage to other side of beam line is clear

Birger and Mike go to other side of beam line

Rachid and George take front handles of spare transport box

Alan take rear handles - Bolek watches

Proceed to beam line under pass and stop

Rachid and George secure grip under box

Rachid and George allow Birger to hold on to handles

Rachid and George let go of box and duck under beam line

Rachid and George holds on to rear part of box

Alan lets go

Rachid and George go to +Z

Upper part is placed on table B

VIII)	Preparation for installation of bottom half

Personnel: Alan, Birger, Rachid, Mike, Bolek, George

Remove detachable section at +Y, -Z area of detector enclosure

Place octagon box at outer half of table A

Rachid into corner next to spectrograph

Table B is pushed into corner as far as possible

Table B is propped up as far as possible

Birger positions support structure onto slide plate, which is placed at the -Z -X corner - line up with marks and checks that all four locknuts are tight

Alan at rear, George at front

Alan and George hold each end of octagon bottom by the handles

Birger unsecures handles and hold bottom down

Alan and George rotate 180 degrees - Alan counter clockwise.

Place back onto bottom plate again

Birger secures handles on plate

Alan and George support bottom half at each end

Birger places mylar sheet on top for protection

Birger removes screws from handles and also remove plastic sheets.

Alan and George rotate assembly 90 deg. And check hand position

Alan and George rotate another 90 deg.

Alan and George move to table B

George hands off to Rachid

Alan places bottom half into support structure - rear first

George helps steer near vertex region

Birger secures bottom half into support structure - two rear screws first

George fastens through pin near vertex

IX)	Installation of bottom half

Personnel: Alan, Birger, Rachid, Mike, Bolek, George

Rachid in corner next to spectrometer

Alan and Birger next to table B

George & Mike on outer side

Bolek reads checklist

Russell observes and guards hallway

Black plastic has been removed from octagon hole into enclosure

Lamp into position between tracks

Rachid guides the front end of octagon

George and Mike observes from other side

Alan and Birger slide the whole structure on table to line up with black plate - no rotation

Alan and George slide/lift support onto black plate and align with beam line in a sliding/rotating motion

Rachid still guides the front - watch beam pipe and enclosure

Mike installs track with one screw

Alan and George slide support sideways into final position

Rachid and Mike observe front end to make sure beam line is not touched by the pin

Mike holds on to black handle on his side

Alan and Birger remove table B and wooden shims on floor

Birger removes counterweight

Rachid and George remove counterweight support, 2 screws each side

Rachid removes inner handle, George holds outer handle

Mike installs last track screws

Rachid and Alan install securing screws through black plate, not tight

Rachid and Alan install adjustment stops and retaining screws

Mike and George remove outer handle

Mike and George install securing screws through black plate

- Alan tightens securing screws on his side

George and Rachid remove front standoff fixture

Birger goes to outer side

Rachid and Birger elevates structure as follows, while George puts upward pressure on rear of support structure and monitors front edge:

a) One turn up on rear chain

b) Follow up with rear lock nuts

c) One turn up on front lock nuts

d) One turn up on front chain.

e) Switch to 1/2 turns for last few turns.

Repeat slowly 30 times in total - Mike keeps count

Secure locking nuts

Check that it is now in the correct position - 393 mm from plate.

X)	Installation of top half

Personnel: Alan, Birger, Rachid, Mike, Bolek, George

Alan, Rachid, Mike on outer side, Russell, George, Bolek on inner side

Upper half in spare transport box on table C facing correctly

Mike and Rachid remove cover from upper half

Mike installs little handle on rear stand off

Alan at front, Rachid in back

Alan and Rachid hold upper half in each end

Place mylar sheet on top for protection

Mike removes handles

George moves to inner side in corner by spectrometer

Mike observes behind Alan

Alan and Rachid slowly move toward final position until Alan's left hand touches enclosure.

George observes and guides on other side

Slide onto guide pins while Rachid guides with left hand, Alan with right hand

PLAN B: In case the pins are on the inner side

- George and Bolek help guide onto the pins

George holds on to front end - Rachid in back

Alan installs screws on both sides

Alan returns to outer side

Alan and George remove stand off in front

Rachid removes stand off in back

Octagon is now safely mounted around the beam pipe.

XI)	Remaining Tasks

- Replace detachable section at +Y, -Z area of detector enclosure

Remove hose clamp and plexiglass plate between tracks

With clamping screws facing out install manifold support screws in from below

Install manifold onto support w. Al spacer between screws and manifold

Replace manifold supply hose and tighten clamp from beneath

Re-install back enclosure plate

Connect supply hoses

Secure outer back plate

Secure inner plate and connect both halves

Connect output hoses

Install support for FEC crates behind octagon

Install FEC crates

- Install 'C'-cables

Survey to ensure that octagon is centered around the beam-line.