## Slide 1: Support for ca_put_callback in synApps
ca_put_callback allows Channel Access clients to write to a PV and wait for a callback to indicate that the entire operation is complete
  The record written to and any linked records using DB or FLNK links (not CA links).
The callback is done when all records have called recGblFwdLink(), normally done at the end of the process() function.
Use of ca_put_callback eliminates the need for polling to determine when an operation is complete
  Essential for use of EPICS sscan record
Some synApps records only call recGblFwdLink when their logical operation is complete
    motor
    scaler
    mca
    swait, sseq, sCalcout, aCalcout (optional wait)
    busy

## Slide 2: Busy record
Identical to bo record with 1 exception
It only calls recGblFwdLink() when the VAL field changes from 1 to 0
Can be used in EPICS databases to signal completion with ca_put_callback() when not using the records on the previous slide.
Writes to the busy record can be from
  Channel Access
  Links in other records in the database
  C/C++ callbacks from asyn drivers and asyn device support

## Slide 3: Example: Write to undulator energy, wait for completion
# This is the energy PV to write to with ca_put_callback
record(ao,"$(P)ID$(xx)_energy") { field(FLNK,"$(P)ID$(xx)_busyOn.VAL PP MS")
}
# This sets the busy record to 1 and forward links to record that sets energy
record(bo,"$(P)ID$(xx)_busyOn") {
field(DOL,"1")
field(OUT,"$(P)ID$(xx)_busy.VAL PP MS")
field(FLNK,"$(P)ID$(xx)_energyPut.VAL PP MS")
}
# This is the busy record
record(busy,"$(P)ID$(xx)_busy") {
}
# This fetches the value from _energy and writes the value to the ID control
record(ao,"$(P)ID$(xx)_energyPut") {
field(OMSL,"closed_loop")
field(DOL,"$(P)ID$(xx)_energy.VAL NPP NMS")
field(OUT,"ID$(xx):ScanEnergy.VAL PP MS")
}
# This monitors the Busy field of the ID control and writes it to busy record
record(bo,"$(P)ID$(xx)_copyBusy") {
field(OMSL,"closed_loop")
field(DOL,"ID$(xx):Busy.VAL CP MS")
field(OUT,"$(P)ID$(xx)_busy.VAL CA MS")
}

## Slide 4: Example: areaDetector wait for plugins
record(bo, "$(P)$(R)Acquire") {
field(DTYP, "asynInt32")
field(OUT, "@asyn($(PORT),$(ADDR=0),$(TIMEOUT=1))ACQUIRE")
field(FLNK, "$(P)$(R)SetAcquireBusy")
info(asyn:READBACK, "1")
}
record(calcout, "$(P)$(R)SetAcquireBusy") {
field(INPA, "$(P)$(R)Acquire NPP")
field(CALC, "A")
field(OOPT, "Transition To Non-zero")
field(OUT, "$(P)$(R)AcquireBusy PP")
}
record(busy, "$(P)$(R)AcquireBusy") {}
record(bi, "$(P)$(R)AcquireBusyCB") {
field(DTYP, "asynInt32")
field(INP, "@asyn($(PORT),$(ADDR=0),$(TIMEOUT=1))ACQUIRE_BUSY")
field(SCAN, "I/O Intr")
}
record(calcout, "$(P)$(R)ClearAcquireBusy") {
field(INPA, "$(P)$(R)AcquireBusyCB CP")
field(CALC, "A")
field(OOPT, "Transition To Zero")
field(OUT, "$(P)$(R)AcquireBusy PP")
}
record(bo, "$(P)$(R)WaitForPlugins") {
field(PINI, "YES")
field(DTYP, "asynInt32")
field(OUT, "@asyn($(PORT),$(ADDR=0),$(TIMEOUT=1))WAIT_FOR_PLUGINS")
}